## Slide 1: Advanced VLSI Chip Design Project: Design and implement ASIC for Neural Network inference engine
P V Rajesh Kumar

## Slide 2: Introduction
Problem Statement
  Design and implement an ASIC for a Neural Network inference engine.
Dataset description
  Semeion Handwritten Digit Dataset semeion.data (UCI ML Repository)
  Reference: https://archive.ics.uci.edu/ml/datasets/semeion+handwritten+digit
Dataset Details:
  Dataset is a 1593 x 256 Matrix
  1593 images contains Train Data: 1100, Test Data: 493
  Each image is 16x16 binary vectorized to 256 bits
  10 Classification outputs one hot encoded (1 out of 10 is 1, rest are 0) at last 10 bits.

## Slide 3: Network Description
Network architecture
    Fully connected Neural Network with feed forward.
    Feed-forward step, where input is fed to the model acting upon the model parameters and operators.
    It generates an output of each layer of the model i.e., activations, finally generating the model output.
    Model parameters supplied are pre-trained using Matlab.
    This model does inference part only.
Network parameters –
    Number of Inputs: 256 bit data representing 16x16 pixels of image
    Number of outputs: 10
    Number of neurons in hidden layer: 40
    Activation function for hidden layer: Leaky RELU
    Output format: One-Hot encoded with 10 bits. LSB to MSB each bit represents the digit recognized from 0 to 9.

## Slide 4: Software Implementation
Tasks performed on MATLAB.
      Chnaged training parameters for Training accuracy: 99.3636%, Test accuracy: 90.8722%
      Created Modal Parameters from Training for above accuracy
      Implemented Fixedpoint representation
      Implemented Inference part for Testing Input data using FixedPoint representation
      Generation of Verilog files for Modal Parameters

## Slide 5: Software Implementation (contd..)
Highlight any optimizations you performed on given code.
      Implemented Fixedpoint conversion
      Made the code configurable for training, FixedPoint bits, Training, RELU Slope, Hidden Nodes, Generate Verilog files dump, Run with FixedPoint or Floating, RELU for FixedPoint.
      Added GUI for test outputs

## Slide 6: Software Implementation (contd..)
Fixed point design approach:
      Bit widths allocated: 16bit. Integer: 8 Fraction:8.
      Total memory needed for weights and biases:
      wire signed [0:15] w12 [0:39][0:255]; //40x256x16 bits: 20480 Bytes
      wire signed [0:15] b12 [0:39]; //40x16 bits: 80 Bytes
      wire signed [0:15] w23 [0:9][0:39]; //10x40x16 bits: 800 Bytes
      wire signed [0:15] b23 [0:9]; //10x16 bits: 20 Bytes
      Total: 21380 Bytes ~ 20.76 KB
      Size of multiplier needed
      %Some points for Fixed point calculations
      % Q point calculations go like this
      % Q8 + Q8 = Q8, % Q32 + Q32 = Q32
      % Q8 * Q8 = Q16, % Q32 * Q32 = Q64
      % Fractional parts calculations with below examples
      % Q16.8 * Q1.0 = Q17.8
      % Q17.8 + Q16.8 = Q17.8
      % Q11.8 * Q17.8 = Q28.16

## Slide 7: Software Implementation (contd..)
Scripting to get HW compatible data.
Added scripts to generate HW Verilog code snippets, for Modal Parameters
  Weights: W12, W23, Biases: B12, B23
These files can be directly used in Verilog & are configurable though global configuration Variables in MATLAB

## Slide 8: Hardware Specifications
Frequency of operation: 20 ns
Latency – For 1 input image, from START signal to DONE signal: 14400nSec
I/Os used in thedesign:
        Input:
          clk: 1bit - Used for Clock
          rst: 1bit - Used for RESET (POSEDGE)
          start: 1bit - Used for giving as signal to start performing inference on the image
          test_img: 256 bits - Input Image data in 256 Bits
        Output:
                done: 1bit - Outputs when the inference is done
                predicted_val: 4 bits - Predicted value based on the input test_img

## Slide 9: Hardware Architecture
High-level design comprises of following steps:
Inputs
  clk (positive edge-triggered CLOCK)
  rst (positive edge-triggered RESET)
  start (positive edge-triggered to START inference)
  Test_img (256 bits test image 16x16 pixels)
Outputs
done (1 bit to signal inference is DONE)
predicted_val (The digit predicted in [0-3] bits range 0 to 9 corresponding to the digit value)
States of operation
Matrix multiply hidden layer weights (w12 x a1 i.e. Matrix Multiplication [40 x 256] * [256 x 1])
Bias add hidden weights (z2 = w12 x a1 +b12 i.e. Matrix addition 40 x 1)
Leaky RELU (On z2 = a2 i.e. 40 x 1)
Matrix multiply output layer weights (w23 x a2 i.e. Matrix Multiplication [10 x 40] * [40 x 1])
Bias add final layer weights (z3 = w23 x a2 +b23 10 x 1 i.e. Matrix addition 10 x 1)
Leaky RELU (On z2 = a3 i.e. 10 x 1)
Find Max of a3 to predict the image (The digit in [0-3] bits range 0 to 9 range.
done bit (signals end of inference is complete)

## Slide 10: Control FSM
FSM
// States of the operations
parameter IDLE = 4'b0000; //IDLE upon RESET & initializes all Regs used in operation & waits for START signal to go to W12 multiply
parameter W12_MULTIPLY = 4'b0001; // Weights W12 Multiply on input Image
parameter B12_ADDITION = 4'b0010; //Add Biases of B12
parameter RELU_STAGE1 = 4'b0011; //Apply LEAKY RELU on the Added Biases
parameter W23_MULTIPLY = 4'b0100; // Weights W23 Multiply on output of LEAKY RELU output
parameter B23_ADDITION = 4'b0101; //Add Biases of B23
parameter RELU_STAGE2 = 4'b0110; //Apply LEAKY RELU on the Added Biases
parameter PREDICTION = 4'b0111; //Predict the value
parameter FINISHED = 4'b1000; //Generate a DONE signal as output

## Slide 11: Control FSM (contd..)

## Slide 12: Hardware Schematic
Picture of Schematic from Genus (post-synthesis)

## Slide 13: HW Simulation
Description of testbench –
                Test Bench gives 10 sample images to the DUT in a loop.
                Input images are sent in a 256 bit array.
                Once the DUT completes operation, DUT sends a DONE signal.
                In Test Bench wait for DONE signal.
                Upon Done, verify the predicted value from One-Hot encoded value of that input Test Data.

## Slide 14: Accuracy Results
Software Accuracy:
  Train data: 99.36365%
  Testing with floating point weights: 90.872211
  Test data with fixed point weights: 89.04665
Accuracy on HW:
  Pre-synthesis: (10 images)
  Post-synthesis: (same 10 images)
  Got stuck at Gate Level Simulation.
If there is an accuracy drop, why has it happened?
Floating to Fixed point conversion causes the error. Increasing the bit width we can achieve more accuracy

## Slide 15: Synthesis Reports
QOR and Power Reports from Synthesis.
POWER
QOR

## Slide 16: LEC Report
Picture of LEC report, and your conclusion from it.
Got stuck at Gate Level Simulation. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 17: Placement
Picture of Placed Design
Got stuck at Gate Level Simulation. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 18: Routing
Picture of Routed Design
Got stuck at Gate Level Simulation. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 19: Post-Routing Reports
Setup and Hold Reports post-route
Power report
Geometry and Connectivity reports
Got stuck at Gate Level Simulation. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 20: Design Highlights
Describe key features/optimizations that you have done that can make your design stand out w.r.t. your peers.
Not found any.

## Slide 21: GDS
Picture of successful GDS streamout from the terminal.
Got stuck at Gate Level Simulation. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 22: Conclusions
Number of neurons in hidden layer = 40
Accuracy on synthesized HW =
Clock Frequency = 20nSec
Latency = 720 Cycles
Initiation Interval =
Total Area =
Total Power (post-routing) =
Setup TNS and WNS (post-routing) = … and ….
Hold TNS and WNS (post-routing) = … and …
NOTE: Keep the format given here. Only fill the values

## Slide 23: Learning Outcomes
What did you learn from this project?
First MATLAB usage to develop HW algorithms as Proof of concept & then implement them in Verilog for HW acceleration.
Cadence tools: Virtuoso for schematics, Genus for Synthesis, Innovus for Place & Route.
Machine Learning basics & processing of a large data in HW for acceleration.
Machine Learning on how to do inference part of a sample test data
Verilog coding differences between FPGA & ASIC for synthesizable code.
Entire ASIC Flow from design to GDS.
Synthesis & LEC issues of the initial Verilog code and how to fix them to make them Synthesizable for ASIC.

## Slide 24: Thank You