## Slide 1: Advanced VLSI Chip Design Project: Design and implement ASIC for Neural Network inference engine
P V Rajesh Kumar

## Slide 2: Introduction
Problem Statement
  Design and implement an ASIC for a Neural Network inference engine.
Dataset description
  Semeion Handwritten Digit Dataset (UCI ML Repository)
  Reference: https://archive.ics.uci.edu/ml/datasets/semeion+handwritten+digit
Dataset Details:
  Dataset is a 1593 x 256 Matrix
  1593 images contains Train Data: 1100, Test Data: 493
  Each image is 16x16 binary vectorized to 256 bits
  10 Classification outputs one hot encoded (1 out of 10 is 1, rest are 0) at last 10 bits.

## Slide 3: Network Description
Network architecture
    Fully connected Neural Network with feed forward.
    Feed-forward step, where input is fed to the model acting upon the model parameters and operators.
    It generates an output of each layer of the model i.e., activations, finally generating the model output.
    Model parameters supplied are pre-trained using Matlab.
    This model does inference part only.
Network parameters –
    Number of Inputs: 256 bit data representing 16x16 pixels of image
    Number of outputs: 10
    Number of neurons in hidden layer: 40
    Activation function for hidden layer: Leaky RELU
    Output format: One-Hot encoded with 10 bits. LSB to MSB each bit represents the digit recognized from 0 to 9.

## Slide 4: Software Implementation
Tasks performed on MATLAB.
      Created Modal Parameters from Training
      Implemented Fixedpoint conversion
      Implemented Inference part for Testing Input data using FixedPoint
      Generation of Verilog files for Modal Parameters
Highlight any optimizations you performed on given code.
      Implemented Fixedpoint conversion
      Made the code configurable for training, FixedPoint bits, Training, RELU Slope, Hidden Nodes, Generate Verilog files dump, Run with FixedPoint or Floating, RELU for FixedPoint.
      Added GUI for test outputs

## Slide 5: Software Implementation (contd..)
Fixed point design approach:
      Bit widths allocated: 16bit. Integer: 8 Fraction:8.
      Total memory needed for weights and biases:
      wire signed [0:15] w12 [0:39][0:255]; //40x256x16 bits: 20480 Bytes
      wire signed [0:15] b12 [0:39]; //40x16 bits: 80 Bytes
      wire signed [0:15] w23 [0:9][0:39]; //10x40x16 bits: 800 Bytes
      wire signed [0:15] b23 [0:9]; //10x16 bits: 20 Bytes
      Total: 21380 Bytes ~ 20.76 KB
      Size of multiplier needed
      %Some points for Fixed point calculations
      % Q point calculations go like this
      % Q8 + Q8 = Q8, % Q32 + Q32 = Q32
      % Q8 * Q8 = Q16, % Q32 * Q32 = Q64
      % Fractional parts calculations with below examples
      % Q16.8 * Q1.0 = Q17.8
      % Q17.8 + Q16.8 = Q17.8
      % Q11.8 * Q17.8 = Q28.16

## Slide 6: Software Implementation (contd..)
Scripting to get HW compatible data.
Added scripts to generate HW Verilog code snippets, for Modal Parameters
  Weights: W12, W23
  Biases: B12, B23
These files can be directly used in Verilog.
And, these files are configurable though global configuration Variables in MATLAB

## Slide 7: Hardware Specifications
Frequency of operation: 20 ns
Latency – For 1 input image, from START signal to DONE signal: 14400nSec
I/Os used in thedesign:
        Input:
          clk: 1bit - Used for Clock
          rst: 1bit - Used for RESET (POSEDGE)
          start: 1bit - Used for giving as signal to start performing inference on the image
          test_img: 256 bits - Input Image data in 256 Bits
        Output:
                done: 1bit - Outputs when the inference is done
                predicted_val: 4 bits - Predicted value based on the input test_img

## Slide 8: Hardware Architecture
HW schematic –

## Slide 9: Control FSM
FSM
// States of the operations
parameter IDLE = 4'b0000; //IDLE upon RESET & initializes all Regs used in operation & waits for START signal to go to W12 multiply
parameter W12_MULTIPLY = 4'b0001; // Weights W12 Multiply on input Image
parameter B12_ADDITION = 4'b0010; //Add Biases of B12
parameter RELU_STAGE1 = 4'b0011; //Apply LEAKY RELU on the Added Biases
parameter W23_MULTIPLY = 4'b0100; // Weights W23 Multiply on output of LEAKY RELU output
parameter B23_ADDITION = 4'b0101; //Add Biases of B23
parameter RELU_STAGE2 = 4'b0110; //Apply LEAKY RELU on the Added Biases
parameter PREDICTION = 4'b0111; //Predict the value
parameter FINISHED = 4'b1000; //Generate a DONE signal as output

## Slide 10: Hardware Schematic
Picture of Schematic from Genus (post-synthesis)

## Slide 11: HW Simulation
Description of testbench –
                Test Bench gives 10 sample images to the DUT in a loop.
                Input images are sent in a 256 bit array.
                Once the DUT completes operation, DUT sends a DONE signal.
                In Test Bench wait for DONE signal.
                Upon Done, verify the predicted value from One-Hot encoded value of that input Test Data.

## Slide 12: Accuracy Results
Software Accuracy:
  Train data: 99.36365%
  Testing with floating point weights: 90.872211
  Test data with fixed point weights: 89.04665
Accuracy on HW:
  Pre-synthesis: (10 images)
  Post-synthesis: (same 10 images)
If there is an accuracy drop, why has it happened?
Floating to Fixed point conversion causes the error. Increasing the bit width we can achieve more accuracy

## Slide 13: Synthesis Reports
QOR and Power Reports from Synthesis.
POWER
QOR

## Slide 14: LEC Report
Picture of LEC report, and your conclusion from it.
Not able to do this. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 15: Placement
Picture of Placed Design
Not able to do this. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 16: Routing
Picture of Routed Design
Not able to do this. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 17: Post-Routing Reports
Setup and Hold Reports post-route
Power report
Geometry and Connectivity reports
Not able to do this. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 18: Design Highlights
Describe key features/optimizations that you have done that can make your design stand out w.r.t. your peers.
No peers able to share.

## Slide 19: GDS
Picture of successful GDS streamout from the terminal.
Not able to do this. But did for counter module.
WorkSpace: /home/client25/Desktop/PVR/ML_Project/

## Slide 20: Conclusions
Number of neurons in hidden layer = 40
Accuracy on synthesized HW =
Clock Frequency = 20nSec
Latency = 720 Cycles
Initiation Interval =
Total Area =
Total Power (post-routing) =
Setup TNS and WNS (post-routing) = … and ….
Hold TNS and WNS (post-routing) = … and …
NOTE: Keep the format given here. Only fill the values

## Slide 21: Learning Outcomes
What did you learn from this project?
First MATLAB usage for HW algorithms development in Verilog
Cadence tools: Virtuoso for schematics, Genus for Synthesis, Innovus for Place & Route.
Machine Learning basics & processing of a large data in HW for acceleration.
Machine Learning on how to do inference part of a sample test data
Verilog coding for FPGA & ASIC.
Entire ASIC Flow from design to GDS.
Synthesis & LEC issues of the Verilog code done and how to fix them.

## Slide 22: Thank You